## Slide 1: INFORMS Annual Meeting Hybrid Modeling for Electricity Policy Assessments
Renato Rodrigues

## Slide 2: Contents
Introduction
How is it different?
How do we do it?
What is it worth?
Conclusions
Introduction How is it different? How do we do it? What is it worth? Conclusions

## Slide 3: Introduction:
  Bottom-up models. (Ex: unit commitment, power expansion planning,…)
  Top-down models. (Ex: CGE models).
  Technology detail in top-down models. (CCGT, wind, nuclear,…)
  Electricity generation market characteristics:
  Geographical;
  Technology;
  Load Block.
  Load block disaggregation allows more complete policy evaluations:
  Average versus marginal prices;
Introduction How is it different? How do we do it? What is it worth? Conclusions

## Slide 4: Introduction
  Case study:
    Active household demand response potential savings in Spain
Chart: Efficiency effect
Original domestic demand | 8081.5763 | 5818.4833 | 3994.2757 | 3495.4911 | 3267.388 | 3358.027 | 3354.3827 | 5101.8029 | 6072.1394 | 6121.6059 | 6767.9251 | 7290.2489 | 8397.172 | 9375.8105 | 9589.8861 | 9077.1659 | 8706.5594 | 9123.4119 | 10383.5722 | 11344.0176 | 11837.7502 | 12977.0961 | 12404.432 | 10531.1662
DR domestic demand | 7081.5763 | 4818.4833 | 3994.2757 | 3495.4911 | 3267.388 | 3358.027 | 3354.3827 | 4601.8029 | 5572.1394 | 5621.6059 | 6267.9251 | 6790.2489 | 7897.172 | 8542.3619 | 8723.3273 | 8082.7545 | 7785.8807 | 8133.6482 | 9177.6996 | 10160.7118 | 10656.1258 | 12897.7615 | 12453.3618 | 10739.8786
Chart: Load displacement effect
Original domestic demand | 8081.5763 | 5818.4833 | 3994.2757 | 3495.4911 | 3267.388 | 3358.027 | 3354.3827 | 5101.8029 | 6072.1394 | 6121.6059 | 6767.9251 | 7290.2489 | 8397.172 | 9375.8105 | 9589.8861 | 9077.1659 | 8706.5594 | 9123.4119 | 10383.5722 | 11344.0176 | 11837.7502 | 12977.0961 | 12404.432 | 10531.1662
DR domestic demand | 7843.8828 | 5693.767 | 5332.9946 | 3362.8006 | 4678.5323 | 6090.6499 | 3539.7816 | 5601.123 | 5494.0506 | 4511.7719 | 4784.2229 | 5365.6232 | 6843.6952 | 8042.3619 | 8223.3273 | 7582.7545 | 7285.8807 | 7633.6482 | 8677.6996 | 9660.7118 | 10156.1258 | 12397.7615 | 11953.3618 | 10239.8786
 |  | Direct effects detail |  | Indirect Effects | 
 |  | efficiency | displacement | efficiency | displacement
BU - electricity model |  | ok | ok |  | 
TD - CGE model |  |  |  | ok | 
TD - CGE with technology |  | ok |  | ok | 
Hybrid | TD - CGE with tech and time | ok | ok | ok | ok
 | Hard link hybrid model | ok | ok | ok | ok
Consumption variation with ADR |  |  | 
Appliance | Displacement | Reduction | ADR actions
Washing machine | 100% | 40% | Full shutdown
Dishwasher | 100% | 40% | ECO program
Dryer | 100% | 20% | Limitations
Water heating | 50% | 30% | stop / partial shutdown
Heating | - | 50% | Unacceptable shutdown
Air_conditioner | - | 50% | Power limitations, thermostat, time zones ...
Others | - | - | Non manageable
Introduction How is it different? How do we do it? What is it worth? Conclusions

## Slide 5: How is it different?
  Literature focused on detailing the electricity production technologies.
  Differences:
    First point: technological disaggregation in Top-down model is insufficient:
      Average price limitation
    Second point: exclusive calibration of Top-down data does not maintain the linkage with bottom-up technological parameters.
      Minimize entropy changes, distance…
What do we do?
  Develop a CGE (Top-down) model capable of load block time disaggregated evaluation
  Reconciliate the data between Top-down and Bottom-up alternatives without any intermediary adjustment stage.
  Develop a completely integrated hybrid model, with the electricity power generation expansion planning and the CGE model formulated as simultaneously solved MCP problems.
Introduction How is it different? How do we do it? What is it worth? Conclusions

## Slide 6: How do we do it?
  Identify costs in the BU model and associated parameters:
  Approximate the technological parameters to reflect the Top-down aggregate
Cost type | Associated technology parameters
Fuel | Thermodynamic efficiency, generated power, fuel price
Variable O&M | Variable O&M costs by technology, generated power
Fixed O&M | Fixed O&M costs by technology, installed capacity
Capital | Overnight costs, construction time, years of amortization, real discount rate, interest rate , installed capacity
Labor | labor use by technology, installed capacity, social contributions
Taxes | Direct and indirect taxes, renewable subsidies,…
Own consumption | electricity own consumption by technology, electricity price
Losses | electricity losses in the grid, electricity price
Pumping | pumping efficiency an generated power, electricity price
Introduction How is it different? How do we do it? What is it worth? Conclusions
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007
fuel price | 24.4162 | 42.6196 | 61.412 | 77.2812 | 92.352 | 95.5947 | 103.4074 | 104.1805
installed capacity | 26.9617 | 41.6944 | 60.096 | 74.5775 | 86.4513 | 104.0806 | 117.6481 | 122.7724
generated power | 24.4964 | 30.8186 | 46.7433 | 48.9472 | 49.6835 | 65.8399 | 71.4036 | 82.2969
CO2 price | 19.4761 | 25.5447 | 37.3543 | 48.3533 | 61.1869 | 71.6041 | 77.6117 | 95.2799
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007
Capital | 32.4729 | 45.2592 | 53.0989 | 56.9108 | 71.8515 | 80.8055 | 84.3981 | 88.3658
Labor | 22.3275 | 38.7252 | 39.5776 | 42.9413 | 56.8155 | 63.2988 | 66.195 | 83.5102
Intermediary inputs | 20.5174 | 39.5712 | 48.3975 | 51.9475 | 52.2082 | 61.8585 | 75.5723 | 92.4056
Total electricity costs
32,000,000 M€

## Slide 7: How do we do it?
  Min-Max formulation:
    Lineal;
    Optimal deviations are estimated to be at the same neighbor.
  Fixed costs distribution by
  load blocks;
    Annual O&M; installed capacity amortization; new capacity installation;…
  Non accounted costs
    Ramp and Startup costs;…
  Market failures:
    Presence of non competitive market power rents; windfall profits;…
Min Max Deviation
Nuclear
p
q
CCGT
Fuel oil
Carbon
Introduction How is it different? How do we do it? What is it worth? Conclusions
Nuclear
p
q
CCGT
Fuel oil
Carbon
Low load
High load

## Slide 8: How do we do it?
Min Max Deviation
power generation operation and expansion
Electricity prices
Fixed costs distribution by load blocks
Non accounted costs and market imperfections rents
Adjusted technology parameters
Extended SAM
with technology and load block disaggregation
Introduction How is it different? How do we do it? What is it worth? Conclusions

## Slide 9: How do we do it?
Min Max Deviation
power generation operation and expansion
Electricity prices
Fixed costs distribution by load blocks
Non accounted costs and market imperfections rents
Adjusted technology parameters
Repeat the process until convergence is reached between technology parameters
Introduction How is it different? How do we do it? What is it worth? Conclusions

## Slide 10: How do we do it?
  Min-Max iterative calibration simulation:
  Quadratic iterative calibration simulation:
Introduction How is it different? How do we do it? What is it worth? Conclusions
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
tdeo_losses_pctg | 0.24358 | 0.22872 | 0.17871 | 0.063505 | 0.076924 | 0.018471 | 0.025597 | 0.0044367 | 0.0073809 | 0.00096565 | 0.0016881 | 0.00028412 | 0.00047036 | 6.1011e-05 | 0.0001066 | 1.7743e-05 | 3.1026e-05 | 3.6602e-06
oem_vom | 0.24358 | 0.22872 | 0.027715 | 0.024058 | 0.0062526 | 0.0070488 | 0.0015514 | 0.002107 | 0.00035511 | 0.00058792 | 7.6306e-05 | 0.00013325 | 2.2387e-05 | 3.7051e-05 | 4.8034e-06 | 8.392e-06 | 1.3967e-06 | 2.4422e-06
oem_fom_labor | 0.24358 | 0.22872 | 0.17871 | 0.063505 | 0.076924 | 0.018471 | 0.025597 | 0.0044367 | 0.0073809 | 0.00096565 | 0.0016881 | 0.00028412 | 0.00047036 | 6.1011e-05 | 0.0001066 | 1.7743e-05 | 3.1026e-05 | 3.6602e-06
oem_fom_social_contribution | 0.24358 | 0.22872 | 0.17871 | 0.063505 | 0.076924 | 0.018471 | 0.025597 | 0.0044367 | 0.0073809 | 0.00096565 | 0.0016881 | 0.00028412 | 0.00047036 | 6.1011e-05 | 0.0001066 | 1.7743e-05 | 3.1026e-05 | 3.6602e-06
oem_fom_equipments | 0.24358 | 0.036524 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
thermodynamic_efficiency | 0.24358 | 0.22872 | 0.17871 | 0.063505 | 0.076924 | 0.018471 | 0.025597 | 0.0044367 | 0.0073809 | 0.00096565 | 0.0016881 | 0.00028412 | 0.00047036 | 6.1011e-05 | 0.0001066 | 1.7743e-05 | 3.1026e-05 | 3.6602e-06
overnight_costs | 0.24358 | 0.22872 | 0.17871 | 0.063505 | 0.076924 | 0.018471 | 0.025597 | 0.0044367 | 0.0073809 | 0.00096565 | 0.0016881 | 0.00028412 | 0.00047036 | 6.1011e-05 | 0.0001066 | 1.7743e-05 | 3.1026e-05 | 3.6602e-06
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6
tdeo_losses_pctg | 0.045742 | 0.022107 | 0.0049271 | 3.8406e-05 | 8.7481e-06 | 6.6012e-07
oem_vom | 0.023049 | 0.011466 | 3.9885e-06 | 8.704e-07 | 5.905e-08 | 0
oem_fom_labor | 0.048483 | 0.021739 | 0.0047134 | 3.7078e-05 | 8.3825e-06 | 7.6516e-07
oem_fom_social_contribution | 0.048483 | 0.021739 | 0.0047134 | 3.7078e-05 | 8.3825e-06 | 7.6516e-07
oem_fom_equipments | 0.22296 | 0.088219 | 2.8305e-05 | 6.1697e-06 | 4.1621e-09 | 2.0865e-08
thermodynamic_efficiency | 0.21273 | 0.07626 | 0.010137 | 0.00018089 | 1.8353e-05 | 3.1959e-07
overnight_costs | 0.77015 | 0.58301 | 0.19585 | 0.0018337 | 0.00041845 | 3.1577e-06

## Slide 11: What is it worth?
  Active household demand response simulation results
Introduction How is it different? How do we do it? What is it worth? Conclusions
Electricity sector direct effects only:
  Quantities for each technology;
  Prices for each load block.
Indirect effects simulation under only one electricity product:
  Fixed quantity change;
  Unique electricity price.
Direct and indirect effects simulation for each load block behavior:
  Quantities for each technology;
  Prices for each load block.
Chart: 
| Nuc | Ncoal | Icoal | CCGT | F-G | Hyd | Wind | ORSR | NRSR | Pump
Electricity Bottom-up model | 0 | 0 | 0 | -0.005671 | -0.33331 | 0 | 0 | 0 | -0.21958 | 0
Chart: 
| Nuc | Ncoal | Icoal | CCGT | F-G | Hyd | Wind | ORSR | NRSR | Pump
CGE Top-down model | -0.0060731 | -0.0060731 | -0.0060731 | -0.0060731 | -0.0060731 | -0.0060731 | -0.0060731 | -0.0060731 | -0.0060731 | -0.0060731
CGE electricity extended model | -0.0064149 | -0.0053181 | -0.0053806 | -0.0078884 | -0.0089728 | -0.0076842 | -0.0073963 | -0.0073682 | -0.0097932 | -0.0072681

## Slide 12: Conclusions:
We presented a method to introduce explicitly load block disaggregation in the CGE formulation
  Described the calibration process which allows the development of a:
    pure CGE geographical, technology and load block disaggregated;
    hybrid integrated CGE and power generation operation expansion model under mixed complementarity formulation.
Advantages of such approach:
  Improved representation of the electricity sector behavior;
  Feasibility of the method;
  Convergence of the algorithm;
  More realistic results for policy evaluations.
Introduction How is it different? How do we do it? What is it worth? Conclusions

## Slide 13
Thank you for your attention!
Questions and comments are welcome!
?